## Slide 1
Control System Simulation
GasTurb 14 Tutorial
Hint: Animations are used to show the functionality of GasTurb in this tutorial. Therefore, please select the presentation mode (Slide Show) to make best use of this tutorial.
To switch from full screen to a window slide show, please select Set Up Slide Show and switch the Show type to Browsed by an individual.

## Slide 2: GasTurb 14 Main Window
For this tutorial we will use a Turbojet.

## Slide 3: We Need Some Data
Select the engine model
Open the engine model

## Slide 4: Off-Design Input Window
The control system protects the engine by limiting temperatures, pressures, spool speeds etc.
Select “Max Limiters”

## Slide 5: Max Limits
You can set switch on several limiters simultaneously. The limiter which restricts the engine most will fix the operating point.
Enter numbers here
Activate the selected limiters
Click the Max
Limiter option
Run the Off-Design cycle

## Slide 6: Solution for Three Active Limiters
Nrel,max=101%
T3,max=650K
Active Limiter
Close the result window
The Turbine Exit Temperature T5 limiter is active,
neither the Spool Speed NH limit nor the Compressor Exit Temperature T3 limit is violated

## Slide 7: Fuel Flow and Thrust as Pseudo Limiters
You may want to run the engine to a given thrust.
Enter the desired thrust
Activate the limiter here
Click the Max
Limiter option
Run the Off-Design cycle

## Slide 8: The Cycle for 25kN Thrust
Thrust = 25kN
Close the result window

## Slide 9: HPC Spool Speed ZXN with Activated Limiters
If any limiter is active, then the Calculation Mode is automatically set to Limits.
The HP Spool Speed ZXN is no longer seen on this page
Click on “Basic Data”

## Slide 10: HPC Spool Speed ZXN with Activated Limiters
Click on “Iteration Variables”
While a limiter is active,
HP Spool Speed ZXN
is an iteration variable

## Slide 11: Limiters And Composed Values
Click on “Formulas”
If you want to consider a limiter which is not on the Limiters page, then define a composed value.

## Slide 12: Limiters And Composed Values
Any Composed Value can be employed as Limiter.
Introduce as a P5Limiter the ratio of P5/P2, for example.
Close the formula window and go to the limiter page

## Slide 13: Limiters And Composed Values
Select the composed value
Enter an example value and activate it
Run the
Off-Design cycle

## Slide 14: Limiters And Composed Values
The P5/P2 limiter is active
Close the result window

## Slide 15: Control Schedules
De-select the P5Limiter
Open “Schedules”
Besides single valued limiters you can also employ
Control Schedules

## Slide 16: Defining a Control Schedule
Select the parameter to be controlled
Select the parameter from which the controlled parameter depends
Enter values
Close the schedule window
Click to activate the Schedule

## Slide 17: Changing Ambient Temperature
Delta T from ISA = 11.85K yields at sea level static conditions T2=300K
Click “alt, Mach, dtamb”
Run the
Off-Design cycle

## Slide 18: T5 Follows the Schedule
Remember:
T2 = 300K yields as scheduled T5 = 1110K.
This slide ends the
Control System Simulation Tutorial