## Slide 1
Component Maps
GasTurb 14 Tutorial
Hint: Animations are used to show the functionality of GasTurb in this tutorial. Therefore, please select the presentation mode (Slide Show) to make best use of this tutorial.
To switch from full screen to a window slide show, please select Set Up Slide Show and switch the Show type to Browsed by an individual.

## Slide 2: GasTurb 14 Main Window
For this tutorial we will use a simple Turbojet

## Slide 3: We Need Some Data
Select the engine model
Open the engine model

## Slide 4: Off-Design Input Data Page
Run an Off-Design simulation without changes

## Slide 5: Off-Design Point Summary
Have a lock at the compressor map
This is the cycle design point, calculated in off-design mode.

## Slide 6: Standard Compressor Map
In this special case – because we have calculated the cycle design point in off-design mode – the yellow square is inside the circle.
Close the result window
The circle marks the cycle design point, the yellow square marks the off-design operating point.
The cycle design point is
Mass Flow W2RStd = 32 kg/s
Pressure Ratio = 12
Efficiency = 0.85
W2RStd = Mass Flow Corrected to Standard Day Conditions

## Slide 7: Off-Design Input Data Page
Click on Special to configure Special Maps
The Standard Maps yield in many cases reasonable trends. However, for accurate simulations the Standard Maps must be replaced by Special Maps.

## Slide 8: HP Compressor Map
In this window you can read the appropriate compressor map from file.
To shorten the tutorial we do not read a special map, we stay with the default map.
At the yellow square the
pressure ratio in the map is 8.3138.
To scale the map in such a way that it fits to the cycle design point (P/P=12) the factor fP/P-1 = 1.504 is applied:
At the yellow square the efficiency in the map is 0.86015.
To scale the map in such a way that it fits to the cycle design point (=0.85) the factors f = 0.9884 and fReynolds=0.9998 are applied:
Peak Efficiency is the highest efficiency found in the scaled map.
The coordinates of the design point in the map (the yellow square) are
Beta,ds = 0.5 and N/sqrt(T),ds = 1
The yellow square marks the cycle design point.

## Slide 9: Map Scaling
At the yellow square the efficiency in the map is now 0.8246.
To scale the map in such a way that it fits to the cycle design point (=0.85) the factors f = 1.03 and fReynolds=0.9998 are applied:
Peak Efficiency is the highest efficiency found in the scaled map. Previously it was 0.8568, now it is 0.8929.
The reason for that is: the cycle design point efficiency remains always 0.85
Close the map window

## Slide 10: Save the data as Engine Model
Click on Operating Line
The data can only be stored as Engine Model File if all data on the Steady State page are identical to those from the cycle design point and if all the Modifiers are zero.
An Engine Model File contains in addition to a normal data file information about the component maps and how they are scaled.
Next we run a single operating line with the default settings.

## Slide 11: Off-Design Input Data Page
Run the Operating Line
Select No
Select Compr

## Slide 12: Compressor Map New
The speed line passing through the cycle design point has the relative corrected speed value of 1.
The numbers at the other speed lines are those from the un-scaled map, divided by N/sqrt(T),ds = 1.05
Peak Efficiency is the highest efficiency found in the map, it is 0.8929.
If we would use the Standard Map with the default setting of the cycle design point
(i.e. Beta,ds = 0.5 and N/sqrt(T),ds = 1),
then the operating line in the compressor map would look as in the next slide.

## Slide 13: Compressor Map Old
The speed line passing through the cycle design point has the relative corrected speed value of 1.
Peak Efficiency is the highest efficiency found in the map, here it is 0.8568.

## Slide 14: Effect of Map Scaling on SFC
Standard Map Scaled With the Default Design Point Coordinates Beta,ds = 0.5 and N/sqrt(T),ds = 1
Standard Map Scaled With the Special Design Point Coordinates Beta,ds = 0.4 and N/sqrt(T),ds = 1.05
This is the cycle design point where both operating lines agree.
Hint:
This slide is made of two pictures which were copied to the clipboard from GasTurb and then pasted into Power Point.

## Slide 15: Comparing Measured Data With GasTurb
And run another Operating line
Switch back to Standard maps

## Slide 16: Read Test Data
Read the file demo_jet.tst
Read a file with measured data
Click Open
Run the Operating Line
Select No

## Slide 17: Making the Comparative Data Visible
Check Show Test Data
Click Plot

## Slide 18: Comparing SFC
Simulation
Measured data
Click on New Picture and plot the isentropic compressor efficiency over the corrected compressor flow

## Slide 19: Comparing Compressor Efficiency
Click on Edit Compr Map
Measured compressor efficiency is higher than in the simulation. For improving the agreement we go for editing the HPC Map.

## Slide 20: The Compressor Map Editor
We will now use the slider to make the lines pass through the middle of the data points.
This line shows the peak efficiency on each speed line
This line shows the efficiency for beta=0.5
These are the measured efficiency data points
Alternatively to using the slider you could edit the peak efficiency values in this column
Click on Speed to modify the speed-mass flow correlation

## Slide 21: The Compressor Map Editor
Similarly we can affect the Speed-Mass Flow correlation by re-labeling the speed lines in the map.
The new compressor map should be saved after closing the map editor

## Slide 22: The Simulation Agrees with the Measurements
After some experiments with editing the map we get a reasonable line-up between the measured data and the simulation.
This slide ends the
Component Maps Tutorial