## Slide 1
Use of Unscaled Maps
GasTurb 14 Tutorial
Hint: Animations are used to show the functionality of GasTurb in this tutorial. Therefore, please select the presentation mode (Slide Show) to make best use of this tutorial.
To switch from full screen to a window slide show, please select Set Up Slide Show and switch the Show type to Browsed by an individual.

## Slide 2: GasTurb 14 Main Window
For this tutorial we will use a Turbojet.

## Slide 3: We Need Some Data
Select the engine file
Open the engine file

## Slide 4: Design Point Input Data Page
Run the Design Point simulation
Set Delta T from ISA to 15K

## Slide 5: Design Point Summary
Close this window
This is the cycle design point.
Close this window, close also the design point input window and switch Off-Design with Standard Maps

## Slide 6: Off-Design Input Data Page
Run the case without modifications

## Slide 7: The Cycle Design Point
Click here to see the Compressor Map
Relative Spool Speed is 1.000
True Spool Speed is 12498 rpm

## Slide 8: Map Reference Corrected Speed and Map Reference Speed
Close this window
The Absolute Corrected Spool Speed is
All values for corrected spool speed in the map are relative to 12185rpm which is the
Map Reference Corrected Speed.
The blades and disks of this compressor are mechanically designed for 12498 rpm. This is the Map Reference Speed of the compressor.
The aerodynamic design of the compressor is done for the compressor inlet temperature of T2 = 303.15K. Since the velocity of sound is higher than on a standard day (T2=288.15K) all the Mach numbers are lower while the compressor is running at 12498rpm. T2 = 288.15K and N = 12185 rpm yield the same Mach number level as T2 = 303.15K and N = 12498 rpm
The yellow square marks the operating point which is in this case the cycle design point.
The Relative Corrected Spool Speed is 1.000

## Slide 9: Off-Design Input Data Page
Click here to open the Operating Line window
Now we will write the scaled compressor map to a file. This can be done from the Operating Line Window.

## Slide 10: Saving a Scaled Map
Write the scaled compressor map and open the file with your favorite editor.
The Map Reference Speed and the Map Reference Corrected Speed are found in that map file
Next we will use this compressor in a turboshaft engine. Close this window and go back to the GasTurb 14 Main Window.
First calculate an operating line

## Slide 11: GasTurb 14 Main Window
Now we use a 2 Spool Turboshaft

## Slide 12: We Need Some Data
Select the engine file
Open the engine file

## Slide 13: Design Point Input Data Page
We will use the same compressor as before. At which point in the map the compressor of the turboshaft engine will operate we can freely select.
Let us choose the same operating point as in the turbojet:
T2 = 303.15K (ISA+15K)
W2Rstd = 32 kg/s
P3/P2 = 12
Isentropic Comp Efficiency = 0.85
Calculate the Design Point

## Slide 14: Design Point Summary
Close this window and switch to Off-Design with Standard Maps
This is how the turboshaft design point data should look like

## Slide 15: Off-Design Input Data Page
Choose Special
Now we will replace the standard compressor map with the map we have inherited from the turbojet.

## Slide 16: Replacing the Standard Map
Select Std Corrected
This is the Standard HPC Map. At the point marked with the yellow square the pressure ratio is 8.3 and the mass flow is 33.5. Note that the scaling factors are all unequal to 1.0
The yellow square marks the map scaling point. If the map is scaled, then this point becomes the cycle design point.
We will now replace this map with the turbojet compressor map we have written to file before.
Click on Compr Map and select the previously stored map

## Slide 17: The map from the turbojet compressor
Check this box to use the map unscaled
Map Reference Speed and Map Reference Corrected Speed are required if the map is being used un-scaled
Close the Special Maps window

## Slide 18: Off-Design Input Window
Run a Single Cycle
Set Delta T from ISA to 0 and HPC Spool Speed to (288.15/303.15)=0.974937.

## Slide 19: Operation on a Standard Day
Click here to see the Compressor Map
The engine runs at the
Map Reference Corrected Speed while T2=288.15K.

## Slide 20: Operation in the compressor map
The operating point is on the speed line N=1, the pressure ratio is 12
This slide ends the
Unscaled Maps Tutorial