## Slide 1
Introduction to Transient Simulations
GasTurb 14 Tutorial
Hint: Animations are used to show the functionality of GasTurb in this tutorial. Therefore, please select the presentation mode (Slide Show) to make best use of this tutorial.
To switch from full screen to a window slide show, please select Set Up Slide Show and switch the Show type to Browsed by an individual.

## Slide 2: GasTurb 14 Main Window
For this tutorial we will use a 2 Spool Turboshaft

## Slide 3: We Need Some Data
Select the engine model
Open the engine model

## Slide 4: Off-Design Input Data Page
Run a Single Cycle with HPC Spool Speed ZXN = 0.8. The transient simulation will begin at this operating point.
Run the Off-Design cycle

## Slide 5: Off-Design Point Summary
At this operating point the shaft power is 308.5kW while at the cycle reference point 934.9 kW are delivered.
Close the result window

## Slide 6: Initialize Transient Simulations
Before beginning with transient simulations, a steady state operating line needs to be calculated. These steady state data will be shown together with the transient simulation results for comparison.
Click here to initialize transient simulations
Select “Initialize Transient”

## Slide 7: Operating Line in the Compressor Map
Before closing this window you can look at all the correlations you are interested in.
Close the window

## Slide 8: Off-Design Input Window Switch to Transient Simulations
Click here to run a transient simulation
Select “Transient”
Select “Transient” to see the transient input window

## Slide 9: Setup a Pilots Lever Schedule
Setup an example Pilots Lever schedule
Select “Add Point”
And click on the marked positions
The schedule can be modified by selecting “Move Point” and “Delete Point”
Click here to start the transient simulation

## Slide 10: Transient Output Overview
Select “Compr”
Gas generator spool speed
Burner exit temperature
Power turbine spool speed
For viewing other results click the
y=f(x). To see the compressor operating line click the Compr tab.
Notes: Pumpgrenze erreicht

## Slide 11: Compressor Map
To begin with a new transient maneuver, close this window, then click Run in the Off-Design Input Window.
Close the window
Steady state operating line
Transient operating line

## Slide 12: Simulations with Disabled Control System
In the previous simulations with
Pilots Lever=f(Time) input
a simple PID controller was active.
If Gas Generator Speed or
Fuel Flow is given as function of time then the control system is disabled.
If you want to make any input quantity a function of time which is not offered in the Time Schedule Input then use a combination of composed values with iteration.
Click on Formulas

## Slide 13: Making any Input Quantity a Function of Time
First, we have to define a table, containing the schedule of our input quantity
Click on Tables

## Slide 14: Making any Input Quantity a Function of Time
Choose time as X-Value and enter numbers for the quantity of interest in the Result row. At time=0 the number must be the same as for the steady state condition at which the transient maneuver begins.
Close the window
Enter a name for the table here (optional)

## Slide 15: Calling a Table as Composed Value
The table will show on the Tables page in the composed values editor.
Insert the table as a formula, then close the window
Close the window

## Slide 16: Define an Iteration…
Click on Iteration

## Slide 17: Define an Iteration…
Close the window
Choose Delta T from ISA as iteration Variable…
…the composed value as iteration Target
…and enter the = sign for the target value
Do not forget to activate the iteration, then close the window

## Slide 18: Run the Simulation…
Select Fuel Step
Now you can run any of the transient simulations. In the following example we use the Fuel Step option. In this option the fuel flow is increased after one second by 10% and remains constant at the new level.
Run the simulation

## Slide 19: Run the Simulation…
In the time span from 5 to 6 seconds the ambient temperature is 20° higher. That yields with constant fuel flow an increase in spool speed and T4.
This slide ends the
Transient Simulation Tutorial