## Slide 1
Introduction to Electric Systems in GasTurb
GasTurb 14
Hint: Animations are used to show the functionality of GasTurb in this tutorial. Therefore, please select the presentation mode (Slide Show) to make best use of this tutorial.
To switch from full screen to a window slide show, please select Set Up Slide Show and switch the Show type to Browsed by an individual.

## Slide 2: Electric Propulsion Systems in GasTurb
Electric Propeller
Generator
Electric Motor
The electric propulsion system is supplied with power from a gas turbine spool connected to the generator of the electric system. Any gas turbine spool can be selected.
Before we start: This is a typical series electric propulsion system, as simulated by GasTurb, connected to a 3-spool turboprop.
Electric Power Distribution
The electric power is converted by power electronic elements.
Finally, the electric power is converted to mechanical power by the electric motor.

## Slide 3: Overview: Electric System Tutorials
The calculation of series electric systems with GasTurb 14 is explained in three tutorials. The first two tutorials focus on isolated design- and off-design calculations of the electric system, independent from the gas turbine:
How to design a series electric propulsion system
Off-Design Calculation of a series electric propulsion system
The third tutorial deals with the combination of a series electric system with a gas turbine and covers the interaction of the two systems:
Coupling a series electric propulsion system with a gas turbine
Electric System Tutorial III
Electric System Tutorial I + II

## Slide 4
How To Design a Series Electric Propulsion System
GasTurb 14
Electric System Tutorial I

## Slide 5: Introduction – Design Algorithm
Electric Propeller
Generator
Power Controller
Inverter
Rectifier
Electric Motor
DC Link
Power Controller
Power Offtake
During the design calculation the electric propulsion system is sized independently of the gas turbine. In this first tutorial we will focus on the design calculation of the electric system and therefore ignore the gas turbine calculation.
Additionally, the Generator Gearbox Input Spool Speed is an input parameter for the electric system design calculation.
The electric motor sizes the electric system, i.e. the electric system is sized so that the power requirement of the electric motor is fulfilled. The propeller of the electric propulsion system is sized accordingly. The Electric Motor Torque and Spool Speed are input parameters.
The Generator Gearbox Input Torque and thereby the power at the gearbox is implicitly given by the other parameters. It is iterated so that the following power balance is fulfilled:

## Slide 6: GasTurb 14 Main Window
A series electric propulsion system can only be selected combined with a gas turbine. Therefore we need to choose a gas turbine even if we are only designing the series electric propulsion system in this tutorial. Series electric propulsion systems can be added to any type of engine in GasTurb, except for the Ramjet.
Now we choose the electric system by selecting Add Electric Prop. System…
A click on Performance in the Engine Design button group starts the calculation.
…and then Series Config. Prop.
Let us begin with a 3-Spool Turboprop architecture.
Let us start with the electric system design calculation in GasTurb 14.

## Slide 7: We Need Some Data…
GasTurb comes with demo data sets for all gas turbines and electric configurations.
We select the demo file Demo3prp_series_electric_prp.C3P which includes all the necessary data for both systems.

## Slide 8: Design Input – Calculation Modes
The Performance Calculation Mode is selected by default. This mode models the electric system on a simple power basis with component efficiencies and power densities as input parameters. This calculation mode is recommended for users unfamiliar with electric systems.
The design input window is now extended by input options for the electric propulsion system.
For the calculation of the electric system, GasTurb offers two different calculation modes.
The More … Calculation Mode uses more sophisticated models for the electric system. This calculation mode is recommended for users, who are already familiar with electric systems.

## Slide 9: Design Input – Performance Mode
Let us start with a short introduction to the Performance Mode, before we get into the More… Mode later on in this tutorial.
All the design parameters for the electric propulsion system can be changed in the Electric Propulsion System Tree View. Input parameters can be set for each component of the electric propulsion system. Before we start our first design calculation, let us have a look at the input parameters of the electric propulsion system components.
The El. System Interface is an input value of the gas turbine and does not affect the electric propulsion system design. Hence we will ignore this parameter for this tutorial.

## Slide 10: Electric Motor Input
The series electric propulsion system is sized according to the power requirement of the electric motor, as shown on the introduction page to this tutorial. The electric motor torque and spool speed define the power of the electric motor. Therefore the dimension of the series electric system can be defined by modifying these two variables.
The efficiency of the electric machine and the attached gear box at design point conditions can be directly defined.
For calculating the mass of the motor and the gear box a mass/power factor can be applied.
Select the Electric Motor tab in the Electric Propulsion System Tree View.

## Slide 11: Electric Power Distribution Input
The efficiency of the electric power distribution can be set with these parameters. The cable length also influences the mass of the system.
It might be needed to include two power controllers, especially if there is a power offtake from the electric system.
For calculating the mass of the components a mass/power factor can be applied.
A Power Offtake from the electric system can be defined.
Select the Electric Power Distribution tab in the Electric Propulsion System Tree View.

## Slide 12: Generator Input
The generator and gear box spool speed at design point conditions are input parameters.
The efficiency and mass/power factors can be defined analogue to the electric motor.
Select the Generator tab in the Electric Propulsion System Tree View.

## Slide 13: Propeller Input
Select the Propeller tab in the Electric Propulsion System Tree View.
The propeller is calculated with the same model that is already available for turboprop engines.
By clicking on El. Maps the component map for the Propeller can be adapted.

## Slide 14: Ambient Conditions Input
Select the Ambient tab in the Electric Propulsion System Tree View.
As the electric propulsion system is sized independently of the gas turbine, specific ambient conditions for the electric propulsion system can be set. The ambient conditions only have an influence on the propeller of the electric propulsion system.

## Slide 15: Design Point Calculation
We click on Design Point to start a first design calculation with the default input parameters.

## Slide 16: Gas Turbine Summary
In addition to the usual gas turbine summary the electric power offtake is shown. This is an input value of the gas turbine calculation and does not affect the electric propulsion system design. We will therefore ignore this result in this tutorial.
Select the Electric Propulsion System tab.

## Slide 17: Electric Propulsion System: Summary
On the page Summary the most important results of the electric propulsion system design calculation can be found. The power, the losses, the efficiency and the mass of each component is listed.
The power requirement of the electric propulsion system design point is shown at the bottom.
The thrust that is achieved at the design point by the propeller of the electric propulsion system is about 5kN.

## Slide 18: Electric Propulsion System: Schematic
The Schematic page shows a schematic representation of the electric propulsion system.
The most important results of the electric propulsion system are presented here.
We click on Overall Schematic.

## Slide 19: Overall Schematic
The Overall Schematic tab shows a schematic representation of the overall system.
Let us return to the input window.
As described in the introduction, the two systems are not connected during design calculation.
The connection of the systems is explained in another tutorial.

## Slide 20: Parametric Study
Let us perform a Parametric Study for the electric propulsion system.

## Slide 21: Parametric Study
All the input parameters for the electric propulsion system are listed and can be used for the parametric study.
We employ
Electric Motor Prescribed Torque as the only parameter for now.
Use these input values for the parametric study.
Click to start the parametric study.

## Slide 22: Parametric Study
Employ the values as visible in the screenshot by dragging them to the corresponding box. Then click Draw y=f(x).
Only values that changed during the parametric study are listed here. As we performed the study on an electric propulsion system design parameter, only electric propulsion system results can be plotted. (The gas turbine design is unchanged)

## Slide 23: Parametric Study
Return to input window by clicking Close.
The study shows that the electric motor sizes the electric system as well as the propeller. Higher torque at the electric motor results in a larger absolute power requirement of the generator and a higher net thrust of the propeller.
The mass of the electric system is increasing linear with the higher power of the electric system.

## Slide 24: More… Mode
There are sophisticated design models for each electric system component. We will have a look at the input parameters of each component on the following pages. A detailed description of each component model can be found in the GasTurb Manual.
Let us now switch the calculation mode and use more sophisticated models for the electric system.
Select the More… Calculation Mode.
When switching the calculation mode the changes made in the previous calculation mode
are not transferred to the new calculation mode. The initial data from the demo file is used instead.

## Slide 25: Electric Motor Input
These variables are needed for the calculation of the dimension and mass of the electric machine.
Select the Electric Motor tab in the Electric Propulsion System Tree View.
Analogue to the Performance calculation mode the electric system is sized according to the power requirement of the electric motor, defined by these two parameters.
The efficiency of the electric machine at design point conditions is directly defined.
These inputs have an influence on the parameters of the equivalent circuit.

## Slide 26: Inverter Input
These parameters only have a direct influence on the efficiency of the Inverter. They can often be found in inverter data sheets.
Select the Inverter tab in the Electric Propulsion System Tree View.
These parameters directly affect both the efficiency and the mass of the Inverter.
The Modulation Factor defines the ratio between the input DC voltage and the output AC voltage of the inverter.
These parameters are only needed for the calculation of the mass of the Inverter.

## Slide 27: DC Link Input – Cable and Power Offtake
These parameters are only needed for the calculation of the dimension and mass of the DC Cable.
This parameter only has a direct influence on the efficiency of the DC Cable.
Select the DC Link tab in the Electric Propulsion System Tree View.
These parameters directly affect both the efficiency and the mass of the DC Cable.
Analogue to the Performance Mode, a Power Offtake can be defined.

## Slide 28: DC Link Input – SSPC(s)
These parameters are only needed for the calculation of the mass of the Power Controller.
These parameters only have a direct influence on the efficiency of the Power Controller.
These parameters directly affect both the efficiency and the mass of the Power Controller.
It might be necessary to set up a second power controller, especially if there is a power offtake from the electric system.

## Slide 29: Rectifier Input
These parameters are only needed for the calculation of the mass of the rectifier.
These parameters only have a direct influence on the efficiency of the rectifier. They can often be found in rectifier data sheets.
Select the Rectifier tab in the Electric Propulsion System Tree View.
These parameters directly affect both the efficiency and the mass of the rectifier.

## Slide 30: Generator Input
Select the Generator tab in the Electric Propulsion System Tree View.
Analogue to the performance mode, the generator spool speed needs to be set as an input parameter.
These parameters are most important for the calculation of the dimension and mass of the electric machine.
The efficiency of the electric machine at design point conditions is directly defined.
These inputs have an influence on the parameters of the equivalent circuit.

## Slide 31: Design Input Data Window
Let us perform a Design Point Calculation in the More… Mode.

## Slide 32: Gas Turbine Summary
The gas turbine output is not affected by the change of the electric propulsion system calculation mode. Select the Electric Propulsion System tab.

## Slide 33: Electric Propulsion System Summary
The results in the summary of the Electric Propulsion System are the same as in the Performance Mode, as we did not change any input parameter yet.
Let us have a look at the more detailed output.

## Slide 34: Electric Propulsion System Detailed Output
On the page Detailed Output more detailed results can be found for each component of the electric propulsion system.
Short Name Nomenclature is used to show the results for the electric propulsion system. By clicking on the variable name a hint will show up, giving some explanation analogue to the gas turbine summary page.

## Slide 35: Parametric Study
Let us perform a Parametric Study with the electric propulsion system, in which we have a closer look at one of the power electronic components.

## Slide 36: Parametric Study
Use these input values for the parametric study.
Click to start the parametric study.
Select the Rectifier.
Let us employ
Rectifier Des. DC Voltage
as the only parameter for this study. The Parameter defines the DC Voltage of the electric system and strongly affects the mass of the electric system.

## Slide 37: Parametric Study
Again, only values that changed during the parametric study are listed here.
Allocate the parameters to the chart by dragging them to the corresponding box. Then click Draw y=f(x).

## Slide 38: Parametric Study
The study shows that the mass of the electric system drops significantly with higher DC Voltages. The reason is that a lower cable diameter can be used with a lower electric current, which reduces the electric system weight.
As the power requirement of the electric motor is not changed during the study, the current within the electric system drops, when higher Voltages are used.

## Slide 39
This slide ends the How To Design a Series Electric Propulsion System tutorial.