## Slide 1
Coupling a Series Electric Propulsion System with a Gas Turbine
GasTurb 14
Electric System Tutorial III
Hint: Animations are used to show the functionality of GasTurb in this tutorial. Therefore, please select the presentation mode (Slide Show) to make best use of this tutorial.
To switch from full screen to a window slide show, please select Set Up Slide Show and switch the Show type to Browsed by an individual.

## Slide 2: Introduction
In Tutorial I and II we focused on the design and off-design calculations of the electric propulsion systems not yet considering the effects on the gas turbine cycle.
Electric System Tutorial I + II
In this tutorial, we will design the gas turbine and electric propulsion system at a common system design point. Then, we will investigate the interaction between the gas turbine and electric propulsion system in off-design calculations.
Electric System Tutorial III
Hint: We recommend to first complete Electric System Tutorial I + II before working on this tutorial.

## Slide 3: Introduction
Generally, the electric propulsion system is designed independently of the gas turbine, which enables sizing the two systems at individual design points. (This was explained in Tutorial I)
In off-design mode, the electric propulsion system and the gas turbine are mechanically coupled. Both are part of one overall system with mutual dependencies: The gas turbine power offtake by the electric system equals the power input of the electric propulsion system; the interface spool speeds are equal.
Note: While the gas turbine and electric system can be designed independently, care should be taken to make them compatible in terms of shaft power transfer and interface spool speed. In this tutorial we will size the systems for the same point of the design mission, so that compatibility in off-design is easily achieved.

## Slide 4: GasTurb 14 Main Window
Now choose an electric propulsion system by selecting Add Electric Prop. System…
A click on Performance in the Engine Design button group starts the calculation.
…and then Series Configuration Prop.
We will begin with a 2-Spool Turboshaft architecture.
Let us start with the electric propulsion system design calculation.

## Slide 5: We Need Some Data…
We load sample data sets that come with the program for both the gas turbine and the electric propulsion system.
We first choose the standard engine demo-file without data for the electric propulsion system Demo_sht.CYS. Then we load data for the electric system.

## Slide 6: We Need Some Data…
Another Read-Dialog opens to choose an electric data file.
There are two demo files included in GasTurb 14 for the series electric propulsion system with a propeller, one for a shaft power offtake of 115kW and one for 1315kW. The gas turbine design we just loaded delivers 820kW of design point shaft power. Therefore, we choose the smaller electric propulsion system.
Select the electric data file Demo_series_electric_prp_115kW.eSERP.

## Slide 7: Design Input Data Window
Select Application in the input data tree view.
We want to design a split hybrid configuration where part of the gas turbine shaft power is transferred to a mechanically connected propeller and the other part is transferred to the propeller via the electric system. First, we add a propeller to the Turboshaft engine.
Add a propeller to the turboshaft engine. For that switch Application to Turboprop.

## Slide 8: Design Input Data Window
The spool from which the power is taken is defined in design mode. We will use the default selection PT Spool.
For this tutorial we choose Elec. PT Spool PWX = 200kW.
Select El. System Interface.
115 kW
200 kW

## Slide 9: Design Input Data Window
Click on Design Point to start the design calculation of both the gas turbine and the electric propulsion system.

## Slide 10: Gas Turbine Summary
The Summary output shows how much power is provided from the PT-Spool for the electric propulsion system.
Select the Electric Propulsion System tab.
200 kW is the value we just set. It is just an assumption at this point and not necessarily what the electric propulsion system will really need – that will depend on its design and operating point.

## Slide 11: Electric Propulsion System Summary
Let us return to the input data window.
The electric propulsion system shaft power demand at its design point is shown at the bottom. It is different from the 200 kW in the gas turbine summary, which we allow due to the independent design points. This creates the possibility to size the gas turbine and electric propulsion system at different points in the design mission.

## Slide 12: Sizing for the same Design Points
For the following part of this tutorial, we will size both systems for the same operating point. This requires equal spool speeds and torques at the mechanical interface in the design calculation. We achieve this by manually adjusting the design inputs accordingly.

## Slide 13: Sizing for the same Design Points
The Nominal PT Spool Speed is 20000RPM.
We defined before that the electric propulsion system is connected to the PT spool. Therefore, let us check the PT spool speed first.
Select Basic Data.

## Slide 14: Sizing for the same Design Points
In this case, the Gen. Gear Box Prescribed Input Speed is already equal to the Nominal PT Spool Speed.
Select the Generator tab.
The generator gear box input shaft is the interface between the electric propulsion system and the gas turbine. Connecting both systems requires equal spool speeds, i.e. the input spool speed of the gear box equaling the Nominal PT Spool Speed.
Generator Gear Box.

## Slide 15: Sizing for the same Design Points
To achieve a common design point, the generator gear box power needs to adapted as well, so that it matches the power offtake from the gas turbine. The generator power itself is no input parameter, however it depends on the electric motor design. An iteration helps us to solve this.
For that we first need to define a composed value. Click on Additional and select Formulas.

## Slide 16: Composed Values Editor
The variables that are defined at the interface of both systems are the input power of the generator gear box GB1PWIn and the electric power offtake EPWXPT of the gas turbine. We define the ratio of these variables as composed value.
The electric power offtake EPWXPT is an input parameter
The gear box power GB1PWIn can be found as output parameter.

## Slide 17: Sizing for the same Design Points
Now, we click on Iterations.

## Slide 18: Sizing for the same Design Points
The previously defined composed value can now be defined as target value for an iteration within the electric system. As variable we employ the Electric Motor Prescribed Torque.
Set the iteration as visible here and switch on the iteration. The electric motor torque will now be varied until the absolute value of the generator gear box power is equal to the gas turbine shaft power offtake by the electric system.
Select Targets to set the composed value as target of the iteration.
The electric motor sizes the electric propulsion system.
El. Mot. Torque
Generator Power

## Slide 19: Sizing for the same Design Points
Calculate the Design Point again with iteration switched on.

## Slide 20: Output with coupled systems
The gas turbine design point did not change. The iteration only affects the electric propulsion system
Click on Electric Propulsion System.

## Slide 21: Output with coupled systems
The electric motor torque is varied until the power of the generator gear box equals the electric power offtake of the gas turbine. Accordingly the generator gear box power is 200kW.
Let us return to the main window again.

## Slide 22: Electric Propulsion System Off-Design
Let us start an off-design calculation now.
Select as Scope
Performance and then click Off Design
A click on Standard Maps begins the off-design calculation.

## Slide 23: Off-Design Input Data Page
Clicking the run button right away without changing any input parameters will calculate an Off Design Point that equals the Design Point.

## Slide 24: Off-Design Point Summary
The content of this summary page is identical to that of the cycle design point.
The electric propulsion system is now connected to the gas turbine.

## Slide 25: Off-Design Point Summary
The electric propulsion system operates at its design point as well. The results in the summary are the same as in Design.
Let us return to the input data page.

## Slide 26: Calculating an Operating Line
Click to start the calculation of the Operating Line.
Let us now investigate the overall system operating behavior. We begin with calculating an operating line of the gas turbine.

## Slide 27: Calculating an Operating Line
Use 15 Points for the operating line.
As usual, the operating line will be calculated by reducing the relative Gas Generator Spool Speed of the gas turbine.
Click Yes, to calculate another operating line.

## Slide 28: Calculating an Operating Line
We will calculate the second operating line without the connection of an electric propulsion system. This can be done by setting the Electric PT Spool PWX to 0kW.
Set the Electric PT spool PWX to 0 for the second line, so that for this operating line, the electric propulsion system is not connected to the gas turbine.

## Slide 29: Calculating an Operating Line
Click on Compr to view the operating line in the compressor map.

## Slide 30: Calculating an Operating Line
The operating lines with and without electric power offtake are equal. The operating line of the compressor is not influenced by the electric power offtake, as the power offtake is defined on the PT spool of the turboprop engine.
However, the operating points with low relative spool speed do not converge, when the gas turbine is connected to the electric propulsion system.
Select the Electric Propulsion System tab.

## Slide 31: Calculating an Operating Line
Click on Y=f(x) to search for the reason for the convergence problems.
As the electric power offtake is constant at 200kW and the PT spool speed is set constant, the operating point of the generator remains unchanged when varying GG spool speeds.
When the electric power offtake of the gas turbine is zero, the torque of the generator becomes zero.

## Slide 32: Calculating an Operating Line
Employ the values as visible in the screenshot by dragging them to the corresponding box. Then click Draw y=f(x).

## Slide 33: Calculating an Operating Line
Here we see why the operating points with low rel. GG Spool Speed and coupled electric propulsion system do not converge: the power turbine is unable to constantly provide 200kW to the electric propulsion system below certain GG spool speeds. This can be mitigated by implementing a better operating strategy, e.g. adjusting GG spool speed depending on shaft power demand, or setting the electric propulsion system power demand based on the gas turbine operating point.
Let us return to the input data page.
200kW Electric Power Offtake

## Slide 34: Calculating an Operating Line
Let us implement the following operating strategy: A fixed share of gas turbine shaft power shall be diverted to the electric propulsion system, the rest drives the turboprop.
We will use an iteration to achieve this. First, let us first define the power share as a composed value.
Click on Formulas.

## Slide 35: Composed Values Editor
Define the ratio of the electric power offtake EPWXPT to the delivered shaft power PWSD as composed value.
Define the composed value as visible here.
The electric power offtake is an input parameter.
The delivered shaft power can be found among the output parameter.

## Slide 36: Calculating an Operating Line
Now, for defining an iteration, click on Iterations.

## Slide 37: Iteration Input Editor
Set Elec. PT Spool PWX as iteration variable.
The composed value can now be defined as target value for an iteration. With this iteration switched on, the relative power offtake will be constant. This should avoid power offtakes exceeding the available shaft power.
Set the iteration as visible here and switch on the iteration.
Select the composed value as target value of the iteration.
By iterating to EPWXPT/PWSD = 0,272 the ratio of power taken from the PT spool is equal to the design point in every operating point.

## Slide 38: Calculating an Operating Line
Calculate the Operating Line again with the iteration switched on.

## Slide 39: Calculating an Operating Line
Click on Operating Line.

## Slide 40: Calculating an Operating Line
Click on Compr to view the operating line in the compressor map.

## Slide 41: Calculating an Operating Line
With the iteration controlling the electric power offtake, all operating points converge. The operating line is still not affected by the electric power offtake.

## Slide 42: Calculating an Operating Line
With the iteration switched on, the electric motor torque is reduced when the HP relative spool speed drops, due to the reduction of the electric power offtake. The relative spool speed of the electric motor is set constant and therefore does not change.
Select the Electric Motor tab.

## Slide 43
This slide ends the Coupling a Series Electric Propulsion System with a Gas Turbine tutorial.