## Slide 1
Off-Design Calculation of a Series Electric Propulsion System
GasTurb 14
Electric System Tutorial II
Hint: Animations are used to show the functionality of GasTurb in this tutorial. Therefore, please select the presentation mode (Slide Show) to make best use of this tutorial.
To switch from full screen to a window slide show, please select Set Up Slide Show and switch the Show type to Browsed by an individual.

## Slide 2: Introduction: Off-Design Calculation
Hint: We recommend to first complete Electric System Tutorial I before working on this tutorial.
While the electric propulsion system and the gas turbine are designed separately, they are always coupled in off-design calculation mode. The generator (mechanical) input power and spool speed then follows from the gas turbine operating point. In this tutorial, we will focus on the electric propulsion system behavior only.
Gas Turbine Spool Speed
Power Offtake by Electric System
There are two parameters at the interface of the gas turbine and the electric propulsion system: The spool speed of the gas turbine spool, with which the electric propulsion system is coupled, and the power offtake by the electric propulsion system. These parameters mainly define the operating point of the generator and the electric propulsion system.

## Slide 3: Introduction: Off-Design Algorithm
The spool speed of the electric motor can be set by the user.
As described before, the generator gear box spool speed and torque are now defined by the gas turbine spool, to which the electric propulsion system is coupled. They can therefore not be directly edited by the user during off-design calculation.
Electric Propeller
Generator
Power Controller
Inverter
Rectifier
Electric Motor
Power Controller
DC Link
Power Offtake
The electric motor torque is defined by the power that is supplied by the gas turbine to the electric propulsion system. The torque and thereby the power of the electric motor is iterated within the electric system, so that the following power balance is fulfilled:

## Slide 4: GasTurb 14 Main Window
Let us begin with a 3-Spool Turboprop architecture...
Select the scope
Performance and then click Off Design.
A click on Standard Maps begins the off-design calculation.
…combined with the Series Configuration Prop.
Let us start with the electric propulsion system off design calculation in GasTurb 14.

## Slide 5: We Need Some Data…
We load sample data sets that come with the program for both the gas turbine and the electric propulsion system.
Select the demo file Demo3prp_series_electric_prp.C3P which includes all the necessary data for both systems.

## Slide 6: Off-Design Input Data Page
The electric motor relative spool speed is a free input parameter that can be defined by the user as explained in the introduction.
Select the Electric Motor tab in the off-design input tree view.
The electric propulsion system is connected to the gas turbine during off design calculations. Therefore there is no separate tree view anymore.

## Slide 7: Off-Design Input Data Page
Select the El. System Interface tab.
The gas turbine power offtake supplied to the electric propulsion system is defined here. This is an input to both the gas turbine and electric propulsion system simulation.
1315,7kW

## Slide 8: Off-Design Input Data Page
Let us look at the calculation results before modifying any of the loaded data. Click Off Design Point to start the off-design calculation.

## Slide 9: Off-Design Point Summary
A note on the one summary page tells us that the electric propulsion system is connected to the gas turbine. Its power (here 1315,7 kW) is not included in the PWSD.
Select the Electric Propulsion System tab.

## Slide 10: Off-Design Point Summary
The electric propulsion system summary shows the most important results of the off-design calculation analogue to the design summary.
In the off-design output for the electric propulsion system, maps for the Generator, the Electric Motor and the Propeller can be found comparable to the compressor and turbine maps.
Click on Propeller Map to view the off-design point of the propeller in the component map.

## Slide 11: Propeller Map
Now click on Electric Motor Map.
The same propeller map as for turboprop engine propellers is used.

## Slide 12: Electric Motor Map
The circle marks the cycle design point,
the yellow square marks the off design operating point.
In this special case the yellow square is inside the circle, because we did not change any input parameters and calculated the cycle design point of the electric propulsion system in off design mode.
Select the Generator Map.

## Slide 13: Generator Map
Let us return to the input data window.
The operating point of the generator is shown in an efficiency map equivalent to the electric motor.
As already explained the electric propulsion system is operated at the design point.

## Slide 14: Off-Design Input Data Page
1000kW (76% of the design power)
Let us run an off-design calculation with a reduced Electric PT Spool PWX of 1000kW.
Click on Off Design Point to start the calculation.

## Slide 15: Off-Design Input Data Page
Select the Electric Propulsion System tab.
As we did not change the input for the gas turbine the gas path parameters are unchanged.
The lower power transfer to the electric propulsion system is only seen in the higher shaft power PWSD and its related parameters FN and TSFC.

## Slide 16: Off-Design Input Data Page
The power taken of the gas turbine is now reduced to 1000kW. As the generator gear box efficiency is 1, the output power of the gear box is 1000kW as well.
Select the Generator Map button.
Due to the reduced power, the thrust generated by the electric propulsion system propeller is reduced from 4.96 kN to 3.97 kN.

## Slide 17: Generator Off-Design Point
The generator operates with reduced torque. Its spool speed is given by the gas turbine and hence unchanged.
Generator operating point for Elec. PT Spool PWX = 1000kW
Design point
Select the Electric Motor Map button.

## Slide 18: Electric Motor Off-Design Point
Electric motor operating point for Elec. PT Spool PWX = 1000kW
Design point
The electric motors operates with reduced torque as well. Its speed is given by the input parameter El. Mot. Rel Spool Speed.
Let us return to the input data window.

## Slide 19: Parametric Study
Click to start a Parametric Study.
How does the motor speed affect electric propulsion system performance? Let us conduct a parametric study.

## Slide 20: Parametric Study
Click to start the parametric study.
Use these input values for the parametric study.
Let us employ Electric Motor relative Spool Speed as only parameter for the parametric study.

## Slide 21: Parametric Study
Click on Electric Propulsion System to have a look at the electric component maps.

## Slide 22: Parametric Study
Select the Electric Motor tab.
All operating points are at the same point in the generator map. The off-design point of the generator does not change its spool speed when modifying the electric motor spool speed.
Let us have a look at the generator map first.

## Slide 23: Parametric Study
The power delivered to the electric motor is approximately constant throughout the modification of the relative spool speed. This leads to a reduction of torque with higher spool speeds.
The relative spool speed of the electric motor is modified in this parametric study
Select the Propeller tab.

## Slide 24: Parametric Study
Let us return to the input window.
When the electric motor spool speed is modified, while power is approx. constant, the power coefficient and advance ratio of the propeller change accordingly.

## Slide 25: Parametric Study
Click to start another Parametric Study.
How does changing the electric power offtake affect the electric propulsion system performance? Let us conduct another parametric study.

## Slide 26: Parametric Study
Click to start the parametric study.
Use these input values for the parametric study.
Employ Elec. PT Spool PWX as parameter for this study.

## Slide 27: Parametric Study
Click on Electric Propulsion System to have a look at the electric component maps.

## Slide 28: Parametric Study
Select the Electric Motor tab.
As the electric power offtake is reduced the absolute value of the generator torque falls. The spool speed stays constant, because the gas turbine spool speed is not affected.
Let us have a look at the generator map first.

## Slide 29: Parametric Study
The generator delivers less electric power which leads to a reduction of torque of the electric motor as well. As the relative spool speed is set as 1.0, the spool speed does not change in this study.
Select the Propeller tab.

## Slide 30: Parametric Study
The power coefficient of the propeller drops with the reduced power offtake.
Select the Y = f(x) tab.

## Slide 31: Parametric Study
Employ the values as visible in the screenshot by dragging them to the corresponding box. Then click Draw y=f(x).
The previously shown maps indicate that the overall efficiency of the electric propulsion system varies with electric power offtake. Let us have a closer look at this, and the electric propulsion system thrust.

## Slide 32: Parametric Study
As we can see, maximum efficiency is achieved at relatively low power offtakes. This is due to the higher efficiency of not fully loaded electric machines (operating with less than maximum torque).
The thrust provided by the electric propulsion system propeller increases with power. The increase is almost linear, with some electric as well as propeller efficiency influences.

## Slide 33
This slide ends the Off-Design Calculation of a Series Electric Propulsion System tutorial